### PSB H+ single batch injection with Accsim on a 160 MeV energy plateau for emittance growth studies

# Accsim version August, 4, 2006

### At 160 MeV Accsim tracking performed during 18.9 ms (18700 turns), with 99999 macro-particles corresponding to 1.1(1013 real particles.

### The total beam intensity is injected on the 1st turn onto a RF bucket with first and second harmonic cavities of 8 kV (h=1) and 7.5 kV (h=2).

### The H+ beam was injected in the middle of the PSB-ring section L1 where (H,V=0 to avoid transverse mismatch and subsequent emittance blow-up. Likewise, the short closed orbit bump (BS1-BS4) was disabled to avoid optics distortions.

### The injected bunch phase and energy half-width have been optimized for longitudinal matching.

### The simulation was made using the working point QH=4.21, QV=4.35.

### The simulation parameter used TSCBUNCH=True to scale the transverse space charge force in line with the local longitudinal bunch density and CHROM1=True to take into account the chromatic linear tune shifts.

### PSB measurement yielded (M. Chanel): (2% loss over 210 ms

### Longitudinal emittance: 0.82 eVs (at 90%) ( 1.03 eVs (at 2()

### Horizontal/vertical physical 2(-emittances at t=0 ms: 102/47 [(m]

### Horizontal/vertical physical 2(-emittances at t=210 ms: 93/52 [(m].

### Evolution of rms normalized emittances [(m] vs turns

Evolution of rms normalized emittance blow-ups [%] vs turns

### Evolution of physical 2(-emittances [(m] vs turns

Evolution of physical 99%-emittances [(m] vs turns

Evolution of rms longitudinal emittances [eVs] vs turns

Evolution of space charge tune shifts vs turns