## Slide 1: PSB H- chicane magnets: Inconel vacuum chamber option & consequences on beam dynamics
E. Benedetto, V. Forte, M. Martini
Thanks: C. Carli, B. Balhan, J. Borburgh, G. Arduini, R. De Maria, L. Deniau, A. Molodozhentsev

## Slide 2: Outline
Introduction & ~order of magnitudes
Simulations
New correction settings
Caveats
Conclusions

## Slide 3: Introduction
Chicane magnets for H- injection
  46mm (j=66mrad), falls linearly to 0mm in 5ms
Proposed corrugated Inconel vac. chamber new baseline
Influence on beam dynamics of induced Eddy currents:
  Delay of ~50us (hp: it is compensated by power supplies)
  Higher order field components (sextupolar)
    Quadrupolar feed-down
    Excitation 3rd order resonance


-
-
BSW4
BSW3
BSW2
BSW1

## Slide 4: Drawings
from W.Weterings, 09/01/13

## Slide 5: Drawings
66 mm
5.5 mm
32 mm
44 mm
Bump height = 46 mm MAX
from W.Weterings, 09/01/13

## Slide 6: Order of magnitude of perturbation
Edge effect (rectangular magnet):
  k1L~ j2/2L~6e-3
Feed-down from sextupole:
  Int(Bdl)~c0+c1 x+c2 x2 +…
  x0=-50mm
   k1L~3.4e-3
Cfr. presentatin by C. Carli 19/11/09 at PSB beam dynamics w. L4 WG

## Slide 7: Extraction BSW multipoles
Sextupolar component from eddy currents
Took k2L=0.084
  assumed constant for 5ms
  the same for the 4 BSW
Quadrupolar component at BSW1 (similar for both chambers) not considered
from B. Balhan
BSW2-3 @ 2.5ms

## Slide 8: Implementation MADX-PTC/PTC-Orbit:
Understand edge effects in PTC
Time-varying fields w. Multipolar components (thanks A. Molodozhentsev)
Misalignments
BSW apertures (they are shifted!)

## Slide 9: The beam
Nb=35e11 (~twice)
Ex,Ey=2, 2.3 um (...normalized are E*=1.20, 1.38um!!!)
Bf=0.56, V1=8kV, V2=6kV, Brhodot=10 Tm/s
Painting horiz and longitud (20 turns)
Cut @ 95% bucket acceptance after 20t-injection to remove uncapured particles (~0.4%) & avoid artifacts

## Slide 10: The beam: tune footprint
DQ~0.5
DQ~0.4
Huge!!!! ..to be an LIU or HL-LHC beam!!!
 more reasonable param under consideration

## Slide 11: RMS emittance evolution vs.Turn
Qv=4.55 (Qh=4.28)
Qv=4.45 (Qh=4.28)
RED: ceramic chamber
GREEN: inconel, only dipole edge compensation
BLUE: inconel, new compensation settings
Vertical
Horizontal
Vertical
Horizontal
Large growth in horizontal…due to (too) large DQ & integer x-ing
  Does it “hide” effect of multipoles?  Check ongoing
  For ISOLDE, Qh needs optimization

## Slide 12: RMS normalized emittances
Vertical
Horizontal
Horizontal
Vertical
Qv=4.55 (Qh=4.28)
Qv=4.45 (Qh=4.28)

## Slide 13: Actual intensity (Nb=17.5e11)

## Slide 14: Actual intensity (Nb=17.5e11)
Qv=4.55 (Qh=4.28)
Qv=4.45 (Qh=4.28)
Horizontal
Vertical
Vertical
Horizontal

## Slide 15: Compensation settings
Extra trims on QDE3, QDE14
Selected for active compensation of Vertical BetaBeating from edge effects (quad. error)
  Cfr many presentation by C.Carli et al. 2009-2011
Used also for perturbation (feed-down from sextupolar errors) in Inconel vac. Chamber
What is left uncorrected:
  Almost no correction for the horizontal plane (what if Qx moves close to 0.5?)
  Feed-down from sextupoles induces also small dipole error  COD of <1mm (not corrected, but could it be adjusted with delays?)

## Slide 16: New settings QDE3,14 and QFO, QDE (w. Q-strips)

## Slide 17: Not taken into account
Transient for the multipoles rise/fall (discontinuities in Bdot)  foresee smooth transition?
Delay (i.e. individual powering would compensate for it), i.e. bump is closed
Quad. component at BS1 (septum), similar for both chambers  could it be reduced with poles shaping?
Case if not perfect compensation ~10% off ( what could be achieved?)
Operation/future beams:
  High intensity (ISOLDE) beams  losses!!!
  A more realistic LIU beam (w. no painting?) with DQ=-(0.2,0.3)

## Slide 18: Summary
Eddy current induced multipoles have an effect and need proper compensation, but do not seems to be a show-stopper
TODO or ongoing:
  Effects of a not perfect compensation should be evaluated (Question: what are the limits of power supplies? What about transients?)
  Simulations for an ISOLDE beam (losses!!!) and for an LHC beam generated with no painting and lower intensity.

## Slide 19
Back-up slides

## Slide 21: “Static” simulations
Ramp @ 2ms (out of 5ms)
Assumed:
  trajectory bump
  edge effects
  multipoles
Correction for the vertical BetaBeating with QDE3, QDE14

## Slide 22: Horiz emittance vs. time

## Slide 23: Vertical emittance vs time