## Slide 1: Recent MD results for nominal SPS and low γt optics: Tune scans and Transverse emittances for single bunches
H. Bartosik, K. Cornelis, A. Guerrero, B. Mikulek, G. Rumolo, Y. Papaphilippou, B. Salvant, E. Shaposhnikova
June 16th, 2011

## Slide 2: Tune scans – Method*
  Goal: study the resonance behaviour around the nominal the working points of the nominal SPS (Q26) and the low γt (Q20) optics on the injection plateau
  Strength of individual resonance lines can be identified from the beam loss rate, i.e. the derivative of the beam intensity at the moment of crossing the resonance
  Vertical tune is scanned from about 0.45 down to 0.05 during a period of 3s along the flat bottom
  Low intensity 4-5e10 p/b single bunches with ε~1.2 μm (“single particle behaviour”) injected at nominal tunes
  Horizontal tune is constant during the same period within a supercycle (scanned from cycle to cycle)
  Tunes are continuously monitored using the BBQ and the beam intensity is recorded with the DC-BCT
* similar method (with beams filling the vacuum pipe) previously applied by G. Franchetti et al. in the PS
Notes: TMCI threshold can be increased by increasing chromaticity or longitudinal emittance

## Slide 3: Tune Scans - Results
Identified resonances in the low γt optics
  normal sextupole resonance Qx+2Qy is the strongest
  skew sextupole resonance 2Qx+Qy quite strong !!??
  normal sextupole Qx-2Qy, skew sextupole resonance at 3Qy and 2Qx+2Qy fourth order resonances visible
Identified resonances in the nominal optics
  normal sextupole resonance Qx+2Qy is the strongest
  Coupling resonance (diagonal, either Qx-Qy or some higher order of this), Qx-2Qy normal sextupole
  skew sextupole resonance 2Qx+Qy weak compared to Q20 case
  It seems that the stop-band width of the vertical integer is stronger than in Q20 optics
Notes: TMCI threshold can be increased by increasing chromaticity or longitudinal emittance

## Slide 4: Recap - measurements from May 10th
Measurement of single bunch emittances
  In scan with “reference” wire scanner BWS.519 at flat top
  Long cycle (~10s injection plateau, ~10s acceleration)
  Losses along the cycle extracted from DC-BCT measurement
Bunch length at flat bottom increasing with intensity
  Τ=2.9ns @ 1.5e11 p/b, Τ=3.5ns @ 3e11 p/b
Emittances in PSB: ~ 1μm < 1.5e11p / ~ 1.1μm @ 2e11p / ~ 1.3μm @ 3e11p
  Well adjusted beam parameters in the PSB!

## Slide 5: Difference compared to 2010 for nominal optics?
No dedicated measurements of emittance as function of intensity in 2010
  In 2010, emittance blow-up in PS was necessary in order to reduce blow-up in the SPS nominal optics
  In low γt optics, no blow-up in PS was necessary
Dedicated measurements in 2011
  2010 results for low γt optics confirmed (or outreached)
  No additional blow-up in PS needed for nominal optics – in general beam is more stable
  First measurement of emittance for high intensity in nominal optics shows promising results - What is different in 2011? Why beam is so much more stable this year?
Nominal SPS optics, end of flat bottom (26 GeV/c)
B. Salvant, 26.5.2011
low γt
450 GeV/c
E. Shaposhnikova, Chamonix 2011
Emittances measured 2010,
intensity corrected for losses

## Slide 6: Latest transverse emittance studies
Previous results interesting, but question remains where the blow-up occurs
  In particular the injected beam parameters were no well known
What is the situation in the nominal optics?
In the last weeks, big effort by BI and OP groups to qualify emittance measurements and cross calibrate wire scanners
  PS wire scanner application was corrected (wrong value of β-function for emittance calculations) and calibrated with local orbit bumps
  emittance measurements in PS can be used now to study blow-up in SPS
Present studies on short cycle with 3.5s flat bottom, no acceleration
  Stable beam conditions by adequate adjustment of chromaticity (for Q26)
Measurements of emittance and intensity at the end of flat bottom
  Biggest effect of emittance blow-up due to space charge expected at flat bottom (biggest space charge tune spread)
  Since there is no acceleration in this cycle, losses due to uncaptured beam not taken into account
  Nominal SPS fractional tunes (20.13, 20.18)/(26.13, 26.18)
  Only “In-Scans” are considered; most measurements done in vertical plane (horizontal gave similar results for a few test samples)

## Slide 7: Results – Vertical emittance
MD4 beam in PSB with 2 turns injected (slightly bigger transverse emittances)
  Transverse emittances between 1.1-1.5 μm, depending on intensity
  Not exaclty the same conditions for beam prepation as in the MD on 10th of May
RF-voltage settings were varied with no sizeable influence on emittance
  Here Q20: 3.9 MV
  Q26: 2 MV
Notes: TMCI threshold can be increased by increasing chromaticity or longitudinal emittance

## Slide 8: Results Q20 – Vertical emittance in PS and SPS
MD4 beam in PSB with 1.1 turns injected (slightly smaller transverse emittances)
Simultaneous measurements of vertical emittance in PS and SPS
  At extraction (just before bunch rotation) in PS using PS-65.V
  At end of flat bottom using SPS-BWS.519
  Here RF-voltage of 5.75 MV in SPS
If calibration of wirescanners between machine is believed  emittance blow-up for intensities above 1.5e11 p/b with peak values of 25% at 3e11 p/b
Notes: TMCI threshold can be increased by increasing chromaticity or longitudinal emittance

## Slide 9: Losses from the SPS DC-BCT
Low γt optics
  Low losses (up to 4% for 3e11 p/b) from injection to end of flat bottom
  Fat intensity profiles even for high intensity but losses at injection increase
  Analysis of losses consistent with small emittance blow-up observation
Nominal optics
  Significantly increasing losses for intensities above 2.5e11 p/b up to 10%
  Losses at injection and along the flat bottom for high intensities

## Slide 10: High intensity tune scan for nominal optics
Tune scan with high intensity small emittance single bunches
  “Space charge” tune scan with an intensity of about 2.5-3e11 p/b and injected emittances of about εn~1.3-1.5μm
  Measuring the emittance at the end of flat bottom as function of injected emittance and the total losses
  First scan of vertical tune with a fixed horizontal tune of Qx~26.18 (to be continued …)
  Further scans for different horizontal tune settings will follow …