## Slide 1: Summary and present status of studies on SPS Q20 optics
H. Bartosik, Y. Papaphilippou
LIS meeting, 5.12.2012

## Slide 2: Outline
Motivation for lower transition energy in SPS (a small recap)
Implications of lower transition energy
Impact of injection dogleg
Single bunch studies and threshold for transverse mode coupling
Recent MD results for 25ns beam
Recent MD results for 50ns beam
First impressions of lower transition energy for ions
Summary

## Slide 3: Motivation for Q20 optics
Known intensity limitations in SPS are due to
  Instabilities leading to emittance blow up and/or beam loss
    Transverse mode coupling instability (TMCI) at injection - single bunch instability in vertical plane for intensities above threshold of 1.6x1011p/b (εL=0.35eVs, τ=3.8ns) and low ξy: Nth~ηεL/βy (for matched voltage)
    Longitudinal instability due to loss of Landau damping, Nth ~ ηε2τ (stationary bucket)
    Electron cloud instability
  Other limitations like beam loading, beam loss, heating of machine elements
Instability thresholds can be raised by increasing slip factor η
  Damping of instabilities due to faster synchrotron motion
Changing integer part of tunes down to 20 (“Q20”)
  Transition energy reduced from γt=22.8 (nominal optics) to γt=18
  Factor of about 3 higher η at injection (1.6 at top energy) compared to nominal optics
Slip factor relative to nominal optics
Nth … Instability threshold
ε … longitudinal emittance
τ … bunch length
η … slip factor

## Slide 4: Implications of using Q20 optics
Available RF voltage and beam transfer to LHC
  Higher RF-voltage in Q20 needed (V~η) for same bucket area  better for beam loading
  RF-voltage limited to 7.5MV (already used in Q26 at flat top)  bunch length at extraction?
  For given longitudinal emittance  longer bunches at extraction (due to limited RF voltage, RF upgrade should help)
  For given bunch length at extraction  smaller longitudinal emittance but similar longitudinal stability in SPS since Nth~ε2ητ and τ~(ε2η/V)1/4  εη-1/2 (however potentially unstable in LHC, to be seen …)
  Also higher voltage of 800MHz Landau cavity needed!
Injection dogleg and beam dump
  Quads in injection region (LSS1) are misaligned to gain aperture for beam dump
  This creates non-closed orbit bump in Q20 optics which presently cannot be corrected at high energy  realign quadrupoles or install high energy orbit correctors
  Potential complication for extraction if not corrected (dispersion beating)
  Trajectory for high energy beam dump going off-center through main quadrupole  less kick downwards in Q20 optics (smaller quadrupole gradient) – but still within foreseen region!
Courtesy E. Shaposhnikova
Calculated voltage programs

## Slide 5: Injection dogleg – beam dump apertures
QDA.117
QDA.119
QFA.118
2xMKDV
3xMKDH
TIDH
TIDVG
QDA.117
QDA.119
QFA.118
2xMKDV
3xMKDH
TIDH
TIDVG
Quads in LSS1 are displaced (“dogleg”) to gain aperture for the beam dump trajectory
  QDA.117, QFA.118 and QDA.119 are displaced in negative direction in both planes such that a closed bump is created in nominal optics (see following slides) - Due to the different phase advance (change of quadrupole gradient) in Q20 optics  this bump is not closed
  Due to the reduced gradient in QFA.118, slightly smaller kick downwards in case of Q20
Worst case in terms of aperture: beam dump at 115GeV
  Lowest energy above “forbidden region”  largest beam size (no problem aperture-wise, plot below shows beam envelop using 6σ transverse and 2.5σ longitudinal)
No aperture limitation,
beam is dumped
“underneath”

## Slide 6: Beam dump trajectory
MKDH and MKDV sweep the beam on high energy beam dump TIDVG
  Dump trajectory is going off-center through quadrupole QFA.118
  Due to weaker quadrupole gradients in Q20, slightly smaller kick downwards (beam is dumped closer to edge of dump block)
Due to intervention on MKDV on electrical feed-through only reduced kicker strength from MKDV available (39kV instead of 47kV)
  Beam must be dumped at least 10mm below edge of TIDVG (≥-27 on SEM grid)
  Still within the good region for both optics, even with reduced voltage
MADX Simulation
Q26 (39kV)
Q20 (39kV)
Good region
Good region
single bunch
1 batch
TIDVG

## Slide 7: Impact of quadrupole displacement in LSS1
Assuming the worst case of no orbit correction
  Small non-closure of orbit in Q26 (per design)
  Huge non-closure for Q20 (due to reduced quad strength, i.e. 30% less gradient)
Potential consequences
  Different injection trajectory (although full corrector strength available  should not be a real problem)
  Could be responsible for spurious dispersion as measured at flat top (no orbit correction) due to big orbit oscillation  not nice for extraction to LHC
Q26 – nominal optics
Q20 – low γt optics

## Slide 8: Dogleg correction using existing orbit correctors
Q20 – low γt optics
Option I (no hardware change apart from adding interlocks)
Horizontal plane
  MDHD.11832: hkick=-15 μrad (20A, present max)
  MDH.11407: hkick= 22.8 μrad (3.5A, present max)
  MDH.12207: hkick= 22.8 μrad (3.5A, present max)
Vertical plane
  MDV.11705: vkick=-12.4 μrad (3.5A, present max)
  MDVA.11904: vkick=-12.4 μrad (3.5A, present max)
Option II (less correctors  less chance of failure, but minor hardware changes)
Horizontal plane
  MDHD.11832: hkick=-50 μrad (17A, but reconfiguration of the 4 coils on this special wide aperture corrector in series and changing power convertor, present max) – under investigation …
Vertical plane
  MDV.11705: vkick=-12.4 μrad (3.5A, present max)
  MDVA.11904: vkick=-12.4 μrad (3.5A, present max)
Q20 – low γt optics

## Slide 9: Single bunch studies – TMCI threshold
Q20 optics
  Numerical simulations predict threshold at 3.2x1011p/b (Nth~η/βy, η is 2.85 times higher but also βy is increased)
  No observation of TMCI up to 3.5x1011p/b for low vertical chromaticity (ξy~0.03)
  Regime of higher intensity remains to be explored systematically
  Further increase of threshold possible by using split tunes: Qx~20 ( low γt) and Qy~26 ( no increase of βy); feasibility to be checked … (interference with LHC QPS?)
Nominal optics Q26
  Sharp losses after ~70 turns for low vertical chromaticity and injected intensity higher than 1.6x1011p/b
  Clearly observed threshold for TMCI
  Higher intensity requires larger vertical chromaticity
  Hard to reach intensity above 2.5x1011p/b

## Slide 10: Nominal optics (Q26) – single bunches
Measurements during preparation for LHC high pile up single bunch MD
  ξy ~0.25 as optimal value to reach around 2.5x1011p/b with small emittance (total losses around 15%)
  Slightly higher intensity (2.8x1011p/b) can be reached with chromaticity of ξy~0.4 however with emittance blowup (data not shown)
  Smaller chromaticity (ξy~0.1) leads to significant losses at injection due to TMCI (data not shown)
  Hard to reach more than 2.5x1011p/b at end of cycle due to losses at injection, even for high chromaticity

## Slide 11: Low γt optics (Q20) – single bunches
Single bunch emittances vs. intensity
  Injected up to 3.3x1011p/b and accelerated to flat top using nominal LHC magnetic cycle (long FB, slow ramp) and low chromaticity (ξy~0.1)
  Working point readjusted to 20.13/20.18 for each intensity
Linear increase of emittance with intensity
  Losses at injection and along flat bottom increasing for intensity above 2x1011p/b (space charge? (ΔQy~0.15), working point optimization for high intensity?)
SPS - Q20
SPS - Q20

## Slide 12: MD session with 25ns beam – November 7th
Injected Intensities around 1.2x1011p/b
  Setup and measurements on 25ns beam in Q20 and Q26 optics
  Slightly higher intensity in Q20 at flat top (Injected intensities the same)
  Higher chromaticity in Q26 may be needed for improving transmission
  Went up to 2 batches at most
Other MD studies during the same session
  E-clouid measurements (M. Taborelli), Studies on transmission from PS to SPS with 25ns beam in Q26 optics (T. Bohl, H. Damerau)
Q26
Q20

## Slide 13: Transverse emittance - 25ns beam (1 batch)
Q20: Measurements with WS.416  εx~2.9μm and εy~2.4μm
Q26: Measurements with WS.416  εx~2.8μm and εy~2.6μm

## Slide 14: Transverse emittance - 25ns beam (2 batches)
Q20: Measurements with WS.416  εx~3μm and εy~2.6μ (only a few measurements …)
Q26: Measurements with WS.416  εx~2.7μm and εy~2.7μm (only a few measurements …)

## Slide 15: Longitudinal stability – 25ns beam (1.2x1011p/b)
Comparing stability for 1 batch of 72 bunches with 1.2x1011p/b injected
  Voltage program for constant bucket area of 0.65eVs, 7MV on flat top and 1.8MV (5.25MV) on flat bottom for Q26 (Q20)
  Beam is unstable in Q26  controlled longitudinal emittance blow-up needed
  Beam stable in Q20 (some bunches show increased dipole oscillations)
  RF-settings remain to be optimized for more batches (in Q20)
Q26 – nominal optics
Q20 – low γt optics

## Slide 16: MD session with 50ns beam – November 9th
Comparing longitudinal stability with around 1.5x1011p/b at flat top (without longitudinal emittance blow-up)
  Extracted intensity systematically higher in Q20 due to better “injection efficiency” (ratio between first intensity seen on SPS-BCT and intensity extracted from PS)
  Transmission in nominal optics may be improved by optimizing chromaticity (zero chromaticity value probably different than usual due to preceding MD1 cycle)
Increased intensity to around 1.9x1011p/b injected
  Maximum intensity at flat top reached in Q20 optics around 1.7x1011p/b (however longitudinally unstable, longitudinal emittance blow-up needed)
Q26 – nominal optics
Q20 – low γt optics

## Slide 17: Comparing transmission
  Clearly better “injection efficiency” (ratio between first intensity seen on SPS-BCT and intensity extracted from PS) in Q20 - chromaticity settings not optimal in Q26 or indication for TMCI?
  Injection efficiency worse for later batches in both optics – optimization needed
  Transmission calculated only from SPS-BCT overestimated (losses within first 10ms not seen)
1 batch, 1.55x1011p/b
1 batch, 1.95x1011p/b
4 batches, 1.95x1011p/b
1 batch, 1.55x1011p/b
4 batches, 1.55x1011p/b
1 batch, 1.95x1011p/b
4 batchES, 1.95x1011p/b
Q26
Q26
Q20
Q20

## Slide 18: Transverse emittance – 50ns 1.5x1011p/b (450GeV)
Q26: WS.416
εx~1.6μm/εy~1.7μm
… on average (spread ±0.2μm)
Q20: WS.416
εx~1.6μm/εy~1.8μm
… on average (spread ±0.3μm)
Bigger spread in measurements (and larger average) with WS.519 due to small number of data points along the beam profile at high energy …
  Many measurements were taken (are still being looked at together with A. Guerrero)

## Slide 19: Longitudinal stability – 50ns beam (1.5x1011p/b) I
Comparing longitudinal stability of 1 batch in single RF system (200MHz)
  Voltage program “comparable” between the two optics – injection with 2MV (5.6MV) in Q26 (Q20) and constant bucket area of 0.6eVs in both cycles along the ramp
  Longitudinal damper gain of 15db (10db) in Q26 (Q20) optics – smaller gain works better in Q20
  Beam becomes unstable in Q26 optics for lower energy compared to Q20 (as expected, since threshold is decreasing with energy and proportional to slip factor η) resulting in large spread of bunch length along the batch
  Usual measures: 800MHz Landau cavity + longitudinal emittance blow-up if needed

## Slide 20: Longitudinal stability – 50ns beam (1.5x1011p/b) II
Comparing longitudinal stability of 1 batch in double RF system
  Best settings found during the MD for Q20 optics (injection at 2.5MV and keeping 4.5MV along flat bottom, voltage of 800MHz cavity V800=0.15V200) – nominal setting for Q26 but with increased voltage in 800MHz (V800=0.15V200)
  Without longitudinal emittance blow-up (used in routine operation for stabilizing beam)
  Unstable during ramp in Q26 for this intensity  emittance blow-up needed
  Stable in Q20 for this intensity (emittance blow-up needed for higher intensities, not presented)
  Longer bunches at extraction in Q20 due to limited RF-voltage (however blow-up needed in nominal optics  bunch length with stable settings will be comparable)
Q26
Q20
Courtesy T. Argyropoulos

## Slide 21: Longitudinal stability – 50ns beam (1.5x1011p/b) III
Q26
Q20
Courtesy T. Argyropoulos
Only small dipole
oscillations
no quadrupole
oscillations
quadrupole
oscillations
big dipole
oscillations
50ns beam at flat top (1 batch, 1.5x1011p/b)
  Without controlled emittance blow-up
  800MHz cavity (V800=0.15V200)
Unstable in Q26
  Phase oscillations - dipole instability
  Bunch length oscillations – quadrupole instability
Stable in Q20
  Small bunch length (emittance) - compatible with LHC bucket
  Emittance sufficient for beam stability in SPS but could be too small for LHC (IBS, stability)
  Margin left for emittance blow-up for higher intensity or if needed for stability in LHC

## Slide 22: Ions
Idea to test Q20 optics for LHC ion beam (Yannis, Django, Gianluigi, Karel)
  LHC ion beam suffers from strong particle loss due to
    intra beam scattering?
    Space charge?
    Resonance crossing due to space charge?
  Q20 optics might improve situation due to
    bigger beam size around the ring due to higher dispersion  smaller space charge tune spread (10-15%), IBS?
MD cycle with 6 injections and Q20 optics
  Started to setup this cycle with similar fractional tunes as in nominal optics (0.28, 0.31)
  Managed to accelerate 6 batches up to flat top
  Emittances at flat top very similar to nominal optics
  Transmission not yet as good as with Q26  further optimization and studies needed
  Slip factor at injection almost the same in Q20 and Q26 (γ~7 far away from transition)

## Slide 23: Transmission
Still higher losses along flat bottom in Q20
  Need to optimize working point?
Same emittance as in Q26 ...
More studies needed
  MD time …
  Calculations about IBS …
Q26
Q20

## Slide 24: Summary
Implications on optics
  Injection Dogleg is creating closed orbit distortion which for now is not corrected – solutions currently under investigation
  No problem for beam dump (even with reduced kick strength for MKDV)
Single bunch
  High intensities up to 3x1011p/b can be accelerated with total losses smaller than 10% and small emittance blow-up
  2.5x1011p/b hard to exceed with Q26 due to losses at injection linked to TMCI even with high chromaticity
25ns
  Promising results in MD session: similar transverse emittances in both optics, but more stable in Q20
  More time needed for optimizing the settings
50 ns
  TMCI might soon become limitation for 50ns beam in SPS as intensity will be increased
  Promising results in Q20 optics – better transmission up to now and better stability in longitudinal plane  less or no longitudinal emittance blow-up required for stability
  As predicted, similar bunch length at extraction in both optics for same stability in SPS (but smaller long. Emittance in Q20)
  Still room for improving the settings for high intensity

## Slide 25: Next steps
Pending issues
  Transverse damper V2 still not working properly (unexpected behavior for high frequencies, hard to adjust delay)
Prepare correction of dogleg using existing correctors during winter stop
Injection into LHC during MD
  Rematching the transfer-lines TI8 and TI2 to the new optics in the SPS  presently ongoing
  Study stability of beams with smaller longitudinal emittance in the LHC and acceptable losses due to longer bunches
Future studies: split tunes
  Integer tune 20 in horizontal plane for lower transition energy
  Keeping the tune in the vertical plane close to 26 for smaller vertical beta function  further increase threshold for vertical instabilities such as TMCI (Nth~ηεL/βy), e-cloud, …
  Feasibility to be checked (potential conflict with LHC QPS) …