## Slide 1
Update on PTC/ORBIT space charge studies in the PSB
LIS meeting 07/05/2012
Vincenzo Forte

## Slide 2
Update on PTC/ORBIT space charge studies in the PSB – Vincenzo Forte *
* Follows Preliminary results of the PTC/ORBIT convergence studies in the PSB - Vincenzo Forte – LIS meeting 14-04-12
Preliminary consideration
This presentation follows the one at LIS meeting on 14-04-2012 (you can find that on my DFS public):
dfs:\\Users\v\vforte\Public\14-04-12_Presentation

## Slide 3
Aim of the study
Preliminary study for finding the optimal conditions for PTC/ORBIT space-charge simulations in terms of convergence and computational costs
How far do we have to push in simulations settings to obtain reasonable results with less computational costs?
Update on PTC/ORBIT space charge studies in the PSB – Vincenzo Forte *
* Follows Preliminary results of the PTC/ORBIT convergence studies in the PSB - Vincenzo Forte – LIS meeting 14-04-12

## Slide 4
Update on PTC/ORBIT space charge studies in the PSB – Vincenzo Forte *
* Follows Preliminary results of the PTC/ORBIT convergence studies in the PSB - Vincenzo Forte – LIS meeting 14-04-12
Logical path
Lattice setup
Inject starting 6-D matched distribution
PTC ORBIT basic settings
RMS emittance
tunes
Adding of space charge Orbit routines
1000 turns tracking
95-99% emittance
Results analysis
Best settings choose
Externally created (MadX, …)
Internally modified (tables)
Externally created (Mathematica, …)
PTC-ORBIT
Plots and tunes footprints

## Slide 5
D.O.E.
We wanted to find the best initial parameter settings for transverse space charge studies, with 2 reference models:
    “with chamber” -> static mesh grid (with “stable” beams)
    “without chamber” -> mesh grid dynamically adapted by the particle extent
Update on PTC/ORBIT space charge studies in the PSB – Vincenzo Forte *
* Follows Preliminary results of the PTC/ORBIT convergence studies in the PSB - Vincenzo Forte – LIS meeting 14-04-12
We used 2 criteria:
  Convergence criterium
  Computational costs criterium

## Slide 6
Update on PTC/ORBIT space charge studies in the PSB – Vincenzo Forte *
* Follows Preliminary results of the PTC/ORBIT convergence studies in the PSB - Vincenzo Forte – LIS meeting 14-04-12
Computational costs criterium – actual engpara situation for 1000 turns…
The space charge mesh doesn’t affect so much the CPU TIME
Clearly, the number of m.particles is the main factor for CPU time and elapsed time increasing
*This is not a proper benchmarking (not all the tests done on the same machines), but just to have a feeling of the situation
16h:46m:43s
23h:8min:53s

## Slide 7
Update on PTC/ORBIT space charge studies in the PSB – Vincenzo Forte *
* Follows Preliminary results of the PTC/ORBIT convergence studies in the PSB - Vincenzo Forte – LIS meeting 14-04-12
Convergence criterium – best case – with chamber
In the case “with chamber” the “RMS Emittance” best case is Nxbins=256 – Nybins=256 with 1000e3 m.p. …but … even 256x256 with 500e3 m.p. is acceptable (half nr. M.p. -> half CPU TIME !)

## Slide 8
Update on PTC/ORBIT space charge studies in the PSB – Vincenzo Forte *
* Follows Preliminary results of the PTC/ORBIT convergence studies in the PSB - Vincenzo Forte – LIS meeting 14-04-12
Convergence criterium – best case – with chamber
In horizontal 95% emittance is better for 1000th – 256 x 256

## Slide 9
Update on PTC/ORBIT space charge studies in the PSB – Vincenzo Forte *
* Follows Preliminary results of the PTC/ORBIT convergence studies in the PSB - Vincenzo Forte – LIS meeting 14-04-12
Convergence criterium – best case – with chamber
In vertical 95% emittance is good enough even for 500 th M.p. – 256 x 256

## Slide 10
Update on PTC/ORBIT space charge studies in the PSB – Vincenzo Forte *
* Follows Preliminary results of the PTC/ORBIT convergence studies in the PSB - Vincenzo Forte – LIS meeting 14-04-12
Convergence criterium – worst case – with chamber
In the case “with chamber” the “RMS Emittance” worst case is Nxbins=64 – Nybins=64 with any number of macroparticles… we clearly see a diverging behavior of RMS emittances…

## Slide 11
Update on PTC/ORBIT space charge studies in the PSB – Vincenzo Forte *
* Follows Preliminary results of the PTC/ORBIT convergence studies in the PSB - Vincenzo Forte – LIS meeting 14-04-12
Convergence criterium – footprints - with chamber
The 256x256-500e3 shows a footprint far from any structural resonance (in particular Montague resonance)
The mesh definition affects the footprint... The 64x64 case (with chamber) seems to be “under-resolution” (unphysical <-> the mesh size is comparable to 1s beam size)

## Slide 12
Update on PTC/ORBIT space charge studies in the PSB – Vincenzo Forte *
* Follows Preliminary results of the PTC/ORBIT convergence studies in the PSB - Vincenzo Forte – LIS meeting 14-04-12
Convergence criterium – RMS Emittance - without chamber
In the case “without chamber” the 64x64 case – 500e3 m.p. is comparable with the best case “with chamber” (256x256 – 1000e3 m.p.) – in the case with 250e3 m.particles (64 x 64 without chamber) we have slightly different results (error order 10^-3)

## Slide 13
Update on PTC/ORBIT space charge studies in the PSB – Vincenzo Forte *
* Follows Preliminary results of the PTC/ORBIT convergence studies in the PSB - Vincenzo Forte – LIS meeting 14-04-12
Convergence criterium – 95-99 x Emittance - without chamber
In the case “without chamber” the 64x64 case – 500e3 m.p. is comparable with the best case “with chamber” (256x256 – 1000e3 m.p.) … The case with 250e3 m.p. has worst results in 99% emittance computation…

## Slide 14
Update on PTC/ORBIT space charge studies in the PSB – Vincenzo Forte *
* Follows Preliminary results of the PTC/ORBIT convergence studies in the PSB - Vincenzo Forte – LIS meeting 14-04-12
Convergence criterium – 95-99 y Emittance - without chamber
Also in vertical transverse, the case “without chamber” the 64x64 case – 500e3 m.p. is comparable with the best case “with chamber” (256x256 – 1000e3 m.p.)

## Slide 15
Update on PTC/ORBIT space charge studies in the PSB – Vincenzo Forte *
* Follows Preliminary results of the PTC/ORBIT convergence studies in the PSB - Vincenzo Forte – LIS meeting 14-04-12
Convergence criterium – footprints – with/without chamber
 | DQx | DQy
500e3 – 64x64 (with chamber) | ~-0.27 | ~-0.40
500e3 – 128x128 (with chamber) | ~-0.20 | ~-0.28
500e3 – 256x256 (with chamber) | ~-0.17 | ~-0.24
500e3- 64x64 (without chamber) | ~-0.16 | ~-0.23

## Slide 16
Update on PTC/ORBIT space charge studies in the PSB – Vincenzo Forte *
* Follows Preliminary results of the PTC/ORBIT convergence studies in the PSB - Vincenzo Forte – LIS meeting 14-04-12
Convergence criterium – footprints – without chamber - why 64x64 mesh points and not more?
RMS emittance & footprints are very similar in 64x64 and 128x128 cases

## Slide 17
Convergence criterium – footprints – without chamber - why 64x64 mesh points and not more?
95% & 99% emittances’ behaviors are also very similar…
Update on PTC/ORBIT space charge studies in the PSB – Vincenzo Forte *
* Follows Preliminary results of the PTC/ORBIT convergence studies in the PSB - Vincenzo Forte – LIS meeting 14-04-12

## Slide 18
Update on PTC/ORBIT space charge studies in the PSB – Vincenzo Forte *
* Follows Preliminary results of the PTC/ORBIT convergence studies in the PSB - Vincenzo Forte – LIS meeting 14-04-12
Convergence criterium – footprints – without chamber - why 64x64 mesh points and not more?
95% & 99% emittances’ behaviours are also very similar…

## Slide 19
Update on PTC/ORBIT space charge studies in the PSB – Vincenzo Forte *
* Follows Preliminary results of the PTC/ORBIT convergence studies in the PSB - Vincenzo Forte – LIS meeting 14-04-12
A longer tracking (2500 turns) example
 | ex | ey
First 1000 turns | 2.806e-7*turn+4.8944 | 3.5784e-6*turn+3.3065
From 1000th to 2500th turn | 6.9244e-7*turn+4.894 | 3.1936e-6*turn+3.3065

## Slide 20
Conclusions and future implementations
We had a good indication for parameter settings in space charge studying with PTC-ORBIT, even using a method (2 ½ D) without boundary conditions.
We will keep both ways for further studies (with and without boundaries) for longer turns (starting from 2500 turns as a few synch. periods)
We will use a new set of parameters for the new simulations, which also will include acceleration, bumps …
Update on PTC/ORBIT space charge studies in the PSB – Vincenzo Forte *
* Follows Preliminary results of the PTC/ORBIT convergence studies in the PSB - Vincenzo Forte – LIS meeting 14-04-12
Parameters | Actual simulations | Future simulations
Intensity | 2.475e12 p.p.bunch | 3.52e12 p.p.bunch*
Norm. emittance | 3/2 mm.mrad | 1.9/1.9 mm.mrad*
Qx-Qy (w. point) | 4.27/4.41 | 4.41/4.46
* Update of achievable beam characteristics at injection in LHC – G. Brennan (slide 6)

## Slide 21
CERN PS Booster study:
‘SHORT-dipole’ vz ‘NORMAL’ PSB lattice  emittance growth analysis …
LIU: Machine imperfection and Space charge effects
Halo formation at the injection energy … losses in realistic Aperture
Effect of the double-harmonic RF system
Benchmarking with existing results of the emittance measurements at the
injection energy (160MeV)
Effects of Basic machine imperfections & resonance correction scheme
Multi-turn injection scheme (with FOIL and ‘painting’ process)
 dynamic variation of the machine properties during the injection process
Acceleration process  ‘time’ scale of the emittance growth …
‘Bare’ working point optimization during injection and acceleration
Alexander Molodozhentsev