## Slide 1: Impact of short dipoles on PSB performance (status)
E. Benedetto
LIS meeting, 07/5/12
Acknowledgements: C. Carli, V. Forte, A. Molodozhentsev, LIU-PSB team, …

## Slide 2: Outline
Motivation: Shorter main dipoles in injection region (BHZ11 and BHZ162) to accommodate the H- injection hardware

## Slide 3
http://psb-machine.web.cern.ch/psb-machine/layout.htm

## Slide 4
B.Goddard

## Slide 5
B.Goddard

## Slide 6
Injected beam
W. Weterings
H- injection baseline
Injected beam

## Slide 7: Outline
Motivation: Shorter main dipoles in injection region (BHZ11 and BHZ162) to accommodate the H- injection hardware
Single particle dynamics:
  Vertical b-beating (w.r.t. existing perturbations)
  3 options studied
  Changes in geometry
Multi-particle (space-charge):
  To do
Just started (Thanks Vincenzo for precious help in PTC-Orbit run set-up!)

## Slide 8: Vertical b-beating if Shorter Dipoles
Qv close to half-integer:
  any quadrupolar perturbation in the vertical…
Different edge focusing:
  kl = tan(y/2)/r vertical focusing @ BHZ edges
  r = (L-DL) /y bending radius
  y = 2p /32 bending angle
Displacement of the edges
  focusing occurs at a different phase
  may be cancellation effects

## Slide 9: New layouts considered
Old BHZ162
(1.677m)
Old BHZ11
(1.677m)
Injection hardware
Short BHZ162
Short BHZ11
Case 0
50 cm
50 cm
Short BHZ162
Short BHZ11
Case 2
25 cm
25 cm
Short BHZ162
Short BHZ11
Case 1
25 cm
25 cm
25 cm
25 cm

## Slide 10: BetaBeating for the different options
s (m)
Db/b
The best is
case 2:
DL=0.25m
center is displaced

## Slide 11: What if only BHZ11 is shorter?
BHZ11+BHZ16
only BHZ11
s (m)
Db/b
case 2:
DL=0.25m
center is displaced
if both:
partial cancellation

## Slide 12: Change of Qv
Qv=4.55
Qv=4.43
Qv=4.55
Qv=4.47
Qv=4.49
s (m)
Db/b

## Slide 13: Compare with chicane perturbation
Tried to compensate 2Qv=9 excitation w. QDE3 & QDE14
Used same MADX matching script as Christian’s for the chicane
CHICANE:
kf = 0.7563 ;
kd = -0.7718 ;
dkd3 = -0.00691 ;
SHORTER DIPOLES:
kf = 0.7566 ;
kd = -0.7732 ;
dkd3 = -0.0006;
Conclusion: Factor 10 lower than chicane perturbation
Vs.

## Slide 14: Compare with existing errors
Compare beta-beating with what we have now in the machine
  i.e. that we correct with QNO correctors
I QNO412L3 = -0.94 A;
I QNO816L3 = -1.77 A;
(klqno412L3 = 1.0/Brho(@50MeV)*0.05/85.0*Iqno412L3)
klqno412l3 = -0.00029 = klqno4= -klqn12
klqno816l3 = -0.00055 = klqno8= -klqn16
Conclusions: same ~order of existing errors in the machine (see next slide)

## Slide 15: Existing errors: cured w. QNOs
Same polarity (wrong)
Opposite polarity, ok
1.2 times the currents
The 2 pairs are orthogonal, so they add-up
The different polarity assure that the correction is not canceled-out, as phase advance between the two is almost 2.25 pi

## Slide 16: Change in geometry
DL
y
d=y/2
d
Dx= DL sin(d) = 24.5mm
Trajectory @ exit of short BHZ16 will be Dx= -24.5mm offset
Add Dx= -10mm offset w.r.t. Linac2
Dxtot = -34.5mm
OTHERS:
Change of Twiss param & Disp. in inj. region:
  - should be taken into account
Change in circumference length:
  to be estimated for completeness
  should be ~negligible w.r.t. extraction bump
r0
r1

## Slide 17: Summary & Outlook
Shorter dipoles option looks feasible for single particle dynamics:
  Perturbation (vert. bbeating) ~same order as existing errors
  (partial cancellation of additional focusing)
Preferred option:
  DL=25 cm shorter + displaced (case 2), both BHZ11 & BHZ162
Change in geometry:
  Dx=~25 (+10) mm offset inward w.r.t. Linac2 injection
  Geometry of injection line & region to be revised
Space charge & break of 16-fold periodicity:
  All resonances become systematic
  May reduce space-charge limit (but perturbation is “small”…)
  Thorough simulations not feasible on short time scale
(presented @LIU-PSB meeting 29/3/2012)

## Slide 18: Space-Charge simulation plan
Break of 16-fold periodicity:
  All resonances become systematic
  May reduce space-charge limit (but perturbation is “small”…)
Plan:
  0. Have simulations running DONE, thanks VF for help!
    Without Space-Charge
    “best case from Vincenzo’s studies
    Same parameters as his, to compare optics (Qx=4.27, Qy=4.41)
    Nb= 2.475e12, no acceleration, Ex=4.9e-6, Ey=3.30e-6 (geometric)
  Emittance growth / Losses w. shorter dipoles STARTED
    Preliminary: very small increase of vertical emittance (Ey=3.315e-6 after 365 turns)
  Emittance growth / Losses w. correction implemented TODO
  Increase complexity simulations (for both config!) TODO
    Acceleration
    Working point above half integer
    Errors , …
Another issue: influence of chicane magnet on main dipoles!
(as discussed w. AM, CC, VF, NM, GA)

## Slide 19: Back-up slides

## Slide 20
Betx
Bety