## Slide 1: Status of the single-bunch feedback system for the SPS/LHC
M. Pivi
C. Rivetta, J. Cesaratto, J. Fox, O. Turgut, S. Uemuda, W. Hofle, U. Wehrle, K. Li, H. Bartosik, G. Rumolo, M. Furman, S. De Santis, R. Secondo, J.-L. Vay
LARP collaboration: SLAC, CERN, LBNL
6 June 2012 - LIS Meeting, CERN

## Slide 2: Single-bunch Feedback system concept
TMCI and electron cloud cause intra-bunch motion in the SPS.
The LARP collaboration and CERN are designing a feedback system to measure the position of several slices in a bunch and control each slice individually by applying correcting electric fields.
Need for high bandwidth to sufficiently sample the bunch

## Slide 3: Feedback system ongoing work
Driving the beam during Machine Development studies
Code development with a single-bunch feedback system
Under development also:
  High bandwidth kicker design
  Analog equalizer for the pick-up system
Design Report

## Slide 4: Machine Development’s goals
MDs goals: Install hardware in the SPS tunnel/ Faraday cage and drive the beam (i.e. excite the beam and measure its response)
Evaluate a method to time properly the kicker signal with the bunch.
Actually installed in the SPS beam line:
  Kicker: exponentially tapered pickup and flipped around, with 200MHz response transfer function

## Slide 5
200 MHz kicker in SPS
Hardware installed in the SPS
Beam excitation system in Faraday cage

## Slide 6
Potential SPS location for the single-bunch feedback system

## Slide 9: MD April results: excited bunch multimode motion. 1 / 2
Precisely timed the kick with a Single Bunch in the machine
Swept a 200MHz sine wave excitation signal from a tune of 0.18 through 0.19 The signal is swept from turn 2000-14000.
delta signal from pick-up shows modal composition at turn 4576
Power spectrum (of 1 bunch slice): excitation of mode 0 at turn
4000 and weekly of mode 1 at
Turn 11000.
Qx=0.183, Qs~0.005
RMS vertical motion

## Slide 10: MD April results: excited bunch multimode motion. 2 / 2
Lower bunch chromaticity, swept the excitation signal from a tune of 0.175 through 0.188. The signal is swept here from turn 2000-17000.
Delta signal from pick-up shows modal composition at turn 13376
Power spectrum (of 1 bunch slice): excitation of modes 0, 1, 2, 3
from turn 9000 to 13000.
No -1 mode observed.
Qx=0.181, Qs~0.004
RMS vertical motion

## Slide 11: animations
C. Rivetta, J. Cesaratto

## Slide 12: MD April
All machine data taken to date has been with a single bunch.
Look forward to measurements exciting a particular bunch in a multi-bunch fill.

## Slide 13: Past work
Experimental observations
  Limitation in intensity (TMCI)
  Limitations in filling patterns (ECI)
  Diagnostic tools: BPM, headtail monitors, emittance monitors, mode analysis
  Stabilisation on a bunch-by-bunch level by transverse damper
High bandwidth feedback (some examples)
  Y. Chin et al.: Intra-bunch feedback system in Jparc (Jp), 50 MHz
  J. Thomson: simplified and idealised feedback model → minimum bandwidth of 300 MHz
  K. Ohmi: high bandwidth feedback simulations → 700 MHz
  M. Pivi: implementation of a realistic feedback system into CMAD
Kevin Li, CERN

## Slide 14: Simulation Code Development
Realistic feedback systems have been included in Head-Tail, C-MAD, Warp simulation codes. At SLAC:
  first in C-MAD (by Pivi, Rivetta). Then
  Head-Tail development (by Li, Pivi)

## Slide 15: Plans for code utilization
Head-Tail comes with different options for the SPS to include electron cloud, TMCI and impedances model.
C-MAD (parallel) includes electron cloud and IBS, and realistic SPS lattice from MAD (beam-ecloud interactions at all ring elements and exact kicker(s) location).
  In CMAD 2 different options to configure the bunch slices: with equal distance or with equal charge (=reduce noise significantly)

## Slide 16: Feedback system design

## Slide 17: Code development: Feedback Design
Intra-bunch feedback includes:
Main Blocks
  Processing Channel: FIR-IIR filters (diagonal by now)
  Filter receiver – (Pick-up, cable, receiver, ADC)
  Filter kicker – (DAC, Amplifier, Cables, Kicker)
  Includes saturation at the receiver and amplifier
  The system has finite dynamic range and realistic input noise floor
Bunch sampling frequency is an adjustable parameter
Noise-Signal-Perturbation injection:
  Receiver
  Amplifier
Measurement of absolute vertical displacement and dipole motion
7 input files characterize the feedback system
Frequency bandwidth: example 200MHz / 1000Mhz

## Slide 18: Multi-particle simulation codes
The multi-particle simulation codes solves:

## Slide 19: Feedback system reduced model – Root-locus (no electron clouds)
Eigenvalues for increased gain of the feedback system.
Exceeding the ideal feedback gain may induce the beam unstable.
The beam is stable within the boundary.

## Slide 20: Kicker frequency response
Different kicker bandwidths implemented in simulations. Kicker actually in SPS has BW=200MHz.

## Slide 21: SPS: Feedback OFF
SPS – feedback in “Open Loop” (OFF)
E-cloud density: 0.5e12e/m3, 1.1e11 ppb

## Slide 26: Spectral mode analysis: Feedback OFF
Evolution of vertical position of bunch slices during 512 turns, e-cloud density 6e11 e/m3
Bunch oscillation modes as a function of cloud density

## Slide 27: SPS: Feedback ON Preliminary Tests
SPS – feedback in Closed Loop” (ON)
E-cloud density: 0.5e12e/m3, 1.1e11 ppb, feedback fixed gain 0.5, BW=200-1000MHz

## Slide 28: SPS: Feedback ON Preliminary Tests
SPS – feedback in Closed Loop” (ON)
E-cloud density: 0.5e12e/m3, 1.1e11 ppb, feedback fixed gain 0.5, BW=200-1000MHz

## Slide 29: Feedback power required
Same scale: Low feedback power is required to stabilize the beam in the presence of electron cloud
Feedback ON: no electron cloud
Feedback ON: ecloud density 5e11/m3
Kick applied to individual bunch slices by the feedback system

## Slide 30: Preliminary tests
500 MHz
1000 MHz
Perturbation:
Electron cloud

## Slide 31: Preliminary tests
200 MHz
700 MHz
Perturbation:
Electron cloud

## Slide 32: Report in preparation
The Working Group will provide CERN with the design report and suggested kicker(s) implementations.
CERN will build the feedback system
  resources needed at CERN (with W. Hofle, LIU)

## Slide 33: Simulation plan and feedback design
Mauro Pivi, CERN/SLAC

## Slide 34: Feedback System Team*
*LARP collaboration: SLAC, LBNL, CERN
Beam excitation and MD tests: Rivetta, Fox, Cesaratto, Uemuda, Turgut, Pivi, Hofle, Wehrle
Simulations: Rivetta, Pivi, Li, Secondo, Vay
  Head-Tail development: Li, Pivi
Kicker design: De Santis, Cesaratto

## Slide 35: Summary
Beam excitation and measurements in the SPS show intra-bunch motion with modes excited
Development of codes (recently Head-Tail) to include single-bunch feedback system
  very promising preliminary results from simulations
  low power levels are required to stabilize the beam with electron cloud interactions
Design Report and long-term R&D plan

## Slide 36: Simulation plan and feedback design
In particular, important steps are:
  Optimize bunch sampling: vary from 8 to 64 (so far, used ideally 64). Smaller the number of samples, less expensive the feedback.
  Include noise in the receiver/kicker
  Include SPS realistic MAD lattice
  Iterate on feedback design

## Slide 37: Kicker available in SPS
Kicker: exponentially tapered pickup and flipped around, with 200MHz response transfer function.
  Tapered for frequency response, smooth the zeroes, but keep 50 Ohms along entire length!
See paper by Linnecar